## Slide 1
Bluetooth MAP-Based SMS Monitoring
and OTP Authentication Security Analysis
Wireless and Mobile Security
University Of Wah
Notes: Welcome to our presentation on Bluetooth MAP-Based SMS Monitoring and OTP Authentication Security Analysis. This research project was conducted as part of our Wireless and Mobile Security course at COMSATS University Islamabad, Wah Campus. Today we will demonstrate how Bluetooth MAP protocol vulnerabilities can expose SMS messages and OTP codes, and discuss the security implications of wireless communication protocols.

## Slide 2
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Project Team Members
Hassan Iftikhar
BS-CY-002
Albash Ahmed
BS-CY-024
Azfar Waqas
BS-CY-013
BS Cyber Security
University Of Wah
BS Cyber Security
University Of Wah
BS Cyber Security
University Of Wah
University Of Wah
2 / 18
Notes: This slide introduces our project team. We are three cybersecurity students from COMSATS University Islamabad, Wah Campus, enrolled in the BS Cyber Security program. Each team member contributed to different aspects of this project including Bluetooth exploitation, web authentication development, dashboard creation, and security analysis.

## Slide 3
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Introduction
Bluetooth Message Access Profile (MAP) enables message exchange between devices over Bluetooth connections.
Widely used in:
Hands-free car systems
Smartwatches and wearables
Automotive infotainment systems
SMS-based OTP authentication remains a common security mechanism for banks, social media, and online services.
This project investigates security vulnerabilities in Bluetooth MAP communication and demonstrates SMS monitoring capabilities.
Research Focus:
Investigating how granted Bluetooth MAP permissions can be exploited to intercept SMS messages, including sensitive OTP authentication codes.
University Of Wah
3 / 18
Notes: This slide provides the introduction to our project. Bluetooth Message Access Profile (MAP) is a Bluetooth protocol that enables message exchange between devices, commonly used in hands-free car systems, smartwatches, and other wearable devices. SMS-based OTP authentication is still widely used by banks, social media platforms, and online services. Our project investigates the security gap where Bluetooth MAP permissions, once granted, can be exploited to monitor SMS messages including OTP codes, potentially compromising two-factor authentication systems.

## Slide 4
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Project Objectives
Investigate MAP Vulnerabilities
Analyze security weaknesses in the Bluetooth Message Access Profile protocol
SMS Message Monitoring
Demonstrate SMS monitoring capabilities via Bluetooth MAP service
OTP Interception Simulation
Simulate OTP authentication interception scenarios in controlled environment
Real-Time Dashboard
Develop Flask dashboard for real-time SMS event visualization
Security Analysis
Analyze security implications and propose mitigation strategies
Awareness Campaign
Raise awareness about wireless communication security risks
Goal: Build a complete security analysis pipeline from Bluetooth exploitation to real-time dashboard visualization and mitigation recommendations
University Of Wah
4 / 18
Notes: This slide outlines our six primary project objectives. We aimed to comprehensively investigate Bluetooth MAP protocol vulnerabilities from discovery to mitigation. Each objective was designed to build upon the previous one, creating a complete security analysis pipeline from Bluetooth exploitation to real-time dashboard visualization and finally to security awareness and mitigation recommendations.

## Slide 5
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Project Overview
End-to-End Security Analysis System for Bluetooth MAP communication
Our system combines:
Bluetooth exploitation tools with modern web authentication
Kali Linux environment with specialized Bluetooth utilities
Firebase OTP authentication for realistic attack simulation
Real-time monitoring dashboard for security demonstration
Environment: Controlled laboratory setup for ethical security research
System Highlights
Bluetooth Exploitation
MAP protocol analysis and SMS interception
OTP Authentication
Firebase-based phone verification simulation
Real-Time Dashboard
Flask-based web interface for live monitoring
Ethical Research
Controlled laboratory environment for security analysis
University Of Wah
5 / 18
Notes: This slide provides a high-level overview of our project. We built an end-to-end security analysis system that combines Bluetooth exploitation tools with modern web authentication. The system operates in a controlled laboratory environment using Kali Linux with specialized Bluetooth tools, integrated with Firebase OTP authentication for realistic simulation, and provides a real-time monitoring dashboard for comprehensive security demonstration.

## Slide 6
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
System Components
■ Hardware
● Bluetooth USB Adapter
● Android Smartphone (Target Device)
● Kali Linux Machine (Attack Platform)
■ Software / Tools
● bluetoothctl, hciconfig, sdptool
● mapAccountHijack (Python MAP client)
● Firebase Authentication
■ Applications & Interfaces
Login Portal
HTML / CSS / JS
Firebase Auth
OTP Verification
MAP Exploit
mapAccountHijack
Dashboard
Flask Web App
University Of Wah
6 / 18
Notes: This slide details the system components used in our project. The hardware layer includes a Bluetooth USB adapter for wireless communication, an Android smartphone as the target device, and a Kali Linux machine as the attack platform. On the software side, we used standard Bluetooth utilities (bluetoothctl, hciconfig, sdptool), the mapAccountHijack Python tool for MAP exploitation, Firebase Authentication for OTP simulation, a Flask-based monitoring dashboard, and an HTML/CSS/JavaScript login portal as the target interface.

## Slide 7
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
System Architecture Diagram
■ Windows Login Portal
■ Firebase Authentication
■ Android Smartphone
■ Bluetooth MAP Service
■ Kali Linux
■ mapAccountHijack
■ Flask Dashboard
User Authentication Interface
SMS Delivery Target
Attack Platform
Security Analysis Display
Legend
■ Normal Flow ■ Target Device ■ Attack
University Of Wah
7 / 18
Notes: This slide shows the complete system architecture diagram. The flow begins with the Windows Login Portal where a user attempts to authenticate. The request goes to Firebase Authentication which sends an OTP via SMS to the Android Smartphone. Our attack system running on Kali Linux uses the Bluetooth MAP Service to connect to the smartphone via mapAccountHijack tool, intercepting the SMS messages. The intercepted data is then displayed on the Flask Dashboard for real-time security analysis.

## Slide 8
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Phase 1 – Bluetooth Setup
PHASE 1 / 5
Setup Steps
1. Configure Kali Linux Environment
Install required Bluetooth packages and dependencies
2. Enable Bluetooth Adapter
Use hciconfig to bring up the Bluetooth interface
3. Set Discoverable Mode
Configure controller visibility using bluetoothctl
4. Verify Adapter Status
Ensure proper USB passthrough and adapter detection
5. Establish Communication
Confirm basic Bluetooth connectivity capability
Key Commands
# Check Bluetooth status
$ hciconfig hci0 status
# Bring up adapter
$ sudo hciconfig hci0 up
# Launch bluetoothctl
$ bluetoothctl
This phase establishes the foundational Bluetooth communication layer required for all subsequent MAP operations.
University Of Wah
8 / 18
Notes: Phase 1 covers the Bluetooth environment setup on Kali Linux. This foundational phase involves configuring the Bluetooth adapter using hciconfig to bring up the interface, setting the controller to discoverable mode using bluetoothctl, and verifying the adapter status. We also needed to ensure proper USB passthrough from the host to the virtual machine, which required installing the VirtualBox Extension Pack. This phase establishes the basic Bluetooth communication capability required for all subsequent phases.

## Slide 9
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Phase 2 – MAP Service Discovery
PHASE 2 / 5
Tools Used
bluetoothctl
Interactive Bluetooth manager
hciconfig
HCI device configuration
sdptool
Service discovery protocol
Discovery Process
1
Scan for Devices
Discover nearby Bluetooth devices
2
Pair with Target
Connect to Android smartphone
3
Discover MAP Service
Use sdptool to find MAP record
4
Get Record Handle
Extract service record handle
5
Map Folder Structure
Identify message folder paths
6
Establish Connection
Set parameters for MAP communication
# Discover MAP service on paired device
$ sdptool browse <device_mac> | grep -A 10 "Message Access"
University Of Wah
9 / 18
Notes: Phase 2 focuses on MAP service discovery. Using bluetoothctl, we scan for nearby Bluetooth devices and identify our target Android smartphone. After pairing with the device, we use sdptool to search for the MAP service record on the target. This reveals the service record handle and the MAP message folder structure, which provides the connection parameters needed for MAP communication. The three primary tools used are bluetoothctl for device management, hciconfig for adapter configuration, and sdptool for service discovery.

## Slide 10
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Phase 3 – SMS Monitoring
PHASE 3 / 5
Tool: mapAccountHijack
Core Functions
SMS Monitoring
Read incoming messages
Folder Access
Navigate message folders
Metadata Retrieval
Sender, timestamp, content
Real-Time Events
Live message interception
Execution Flow
1. Connect to target device MAP service using discovered service record
2. Access SMS message folders: inbox, sent, drafts
3. Retrieve message metadata: sender number, timestamp, content preview
4. Monitor real-time SMS events as messages arrive on target device
University Of Wah
10 / 18
Notes: Phase 3 is the core SMS monitoring phase where we use the mapAccountHijack tool to actively exploit the Bluetooth MAP service. This Python-based tool connects to the target device's MAP service and provides several capabilities: SMS monitoring to read incoming and outgoing messages, folder access to navigate through inbox, sent, and drafts folders, metadata retrieval to get sender information and timestamps, and real-time event monitoring to capture new messages as they arrive. This phase demonstrates the actual security vulnerability of Bluetooth MAP permissions.

## Slide 11
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Phase 4 – OTP Authentication Simulation
PHASE 4 / 5
Technologies Used
HTML
CSS
JavaScript
Firebase Auth
Portal Features
Login
User authentication with phone number
OTP Verification
SMS code validation for secure access
Forgot Password
Account recovery via phone verification
Password Reset
Secure credential update mechanism
This portal demonstrates how OTP codes sent via SMS can be intercepted through Bluetooth MAP monitoring.
Authentication Flow
1 User enters phone number on login portal
2 Firebase sends OTP via SMS
3 Bluetooth MAP intercepts SMS
4 Dashboard displays intercepted OTP
5 Attacker gains unauthorized access
University Of Wah
11 / 18
Notes: Phase 4 covers the OTP authentication simulation. We built a responsive login portal using HTML, CSS, and JavaScript with a modern UI design. The portal integrates Firebase Authentication for phone-based OTP verification, simulating a real-world authentication flow. The features include a login page, OTP verification screen, forgot password functionality, and password reset capability. This phase demonstrates how OTP codes sent via SMS can be intercepted by our Bluetooth MAP monitoring system, highlighting the vulnerability of SMS-based two-factor authentication.

## Slide 12
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Phase 5 – Flask Dashboard
PHASE 5 / 5
Real-Time Event Display
Live visualization of intercepted SMS messages as they arrive on the target device
Timestamp Logging
Accurate time tracking for each intercepted message and security event
SMS Activity Monitoring
Message counters, sender identification, and content preview tracking
Security Analysis Dashboard
Threat metrics, risk assessment, and vulnerability scoring display
Technical Implementation
● Built with Python Flask framework
● HTTP JSON communication with mapAccountHijack
● WebSocket-like real-time updates
● Visual timeline of intercepted messages
● Security metrics and threat analysis
● Responsive web interface design
● Event filtering and search capability
● Export functionality for reports
University Of Wah
12 / 18
Notes: Phase 5 covers the Flask Dashboard development. We built a comprehensive real-time monitoring dashboard using the Python Flask framework. The dashboard communicates with the mapAccountHijack tool via HTTP JSON endpoints to receive intercepted SMS data. It provides real-time event display showing incoming messages as they are intercepted, timestamp logging for each event, SMS activity monitoring with message counters, and an overall security analysis dashboard with threat metrics. This component serves as the visualization layer that makes the security vulnerabilities tangible and demonstrable.

## Slide 13
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Problems Faced During Development (Part 1)
# | Problem | Cause | Solution
1 | Bluetooth Adapter Not Detected | VirtualBox USB passthrough failure | Installed VirtualBox Extension Pack and manually attached adapter
2 | Device Not Available | Phone not discoverable or paired | Enabled discoverability and paired using bluetoothctl
3 | Python Dependency Errors | Kali Linux package restrictions | Created virtual environment and installed dependencies manually
4 | MAP Tool Installation Issues | Python compatibility and missing modules | Installed required modules and adjusted environment
University Of Wah
13 / 18
Notes: This slide presents the first set of problems we encountered during development. Problem 1 was the Bluetooth adapter not being detected in VirtualBox, which we solved by installing the VirtualBox Extension Pack and manually attaching the USB adapter. Problem 2 involved the phone not being discoverable, resolved by enabling discoverability and pairing via bluetoothctl. Problem 3 was Python dependency errors due to Kali Linux package restrictions, which we fixed by creating a virtual environment. Problem 4 involved MAP tool installation issues related to Python compatibility, solved by installing required modules and adjusting the environment.

## Slide 14
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Problems Faced During Development (Part 2)
# | Problem | Error | Cause | Solution
5 | Bluetooth Service Failure | No such device | USB adapter disconnected | Reattached adapter and restarted Bluetooth service
6 | Firebase SMS Testing Limitation | No real SMS | Testing mode does not send real SMS | Used testing OTPs and separate controlled SMS demonstrations
7 | Dashboard Not Showing Events | No data | Backend communication mismatch | Implemented HTTP JSON communication between mapAccountHijack and Flask Dashboard
Key Learning: Each challenge provided valuable insights into Bluetooth protocol behavior, virtualized hardware integration, and inter-process communication design.
University Of Wah
14 / 18
Notes: This slide presents the second set of problems encountered. Problem 5 was a Bluetooth service failure with "No such device" error, caused by the USB adapter disconnecting, which we fixed by reattaching and restarting the Bluetooth service. Problem 6 was Firebase's SMS testing limitation - Firebase testing mode does not send real SMS messages, so we used testing OTPs and separate controlled SMS demonstrations. Problem 7 was the dashboard not showing events due to backend communication mismatch between mapAccountHijack and Flask, which we resolved by implementing HTTP JSON communication between the components.

## Slide 15
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Security Analysis
Identified Threats
SMS Metadata Exposure
OTP Exposure
Bluetooth Trust Abuse
Unauthorized Pairing
Excessive Permissions
Authentication Weaknesses
Wireless Communication Risks
Risk Severity Analysis
Chart: 
| SMS Metadata | OTP Exposure | Trust Abuse | Unauthorized Pair | Excess Permissions | Auth Weakness | Wireless Risks
Severity Score | 75 | 95 | 70 | 60 | 65 | 85 | 55
Impact Assessment
Critical: OTP Exposure enables complete account takeover of SMS-based 2FA systems
High: SMS Metadata and Authentication Weaknesses expose sensitive user information
Medium: Trust Abuse and Excessive Permissions create persistent attack vectors
University Of Wah
15 / 18
Notes: This slide presents our comprehensive security analysis. We identified seven major threat vectors: SMS Metadata Exposure where attackers can read message sender and timestamp information, OTP Exposure allowing interception of authentication codes, Bluetooth Trust Abuse exploiting previously granted permissions, Unauthorized Pairing through social engineering, Excessive Permissions where MAP access grants more capability than needed, Authentication Weaknesses in SMS-based OTP systems, and general Wireless Communication Risks inherent to Bluetooth protocols. The risk analysis chart visualizes the severity of each threat.

## Slide 16
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Mitigation Strategies
Disable Bluetooth
Turn off Bluetooth when not actively needed
Remove Trusted Devices
Delete unused paired devices from your phone
Restrict MAP Permissions
Limit Message Access Profile permissions
Use Authenticator Apps
Replace SMS OTP with app-based 2FA
Hardware Security Keys
Use physical keys for critical accounts
Stronger MFA
Implement multi-factor beyond SMS
User Awareness
Educate users about Bluetooth security risks
Regular Audits
Periodically review Bluetooth pairings
University Of Wah
16 / 18
Notes: This slide presents the mitigation strategies to address the identified Bluetooth MAP and OTP security vulnerabilities. These recommendations include: disabling Bluetooth when not needed to reduce attack surface, removing unused trusted devices to prevent abuse of old pairings, restricting MAP permissions on smartphones to limit exposure, using authenticator apps instead of SMS OTP, adopting hardware security keys for critical accounts, implementing stronger multi-factor authentication beyond SMS, and promoting user awareness about Bluetooth security risks.

## Slide 17
TEAM | INTRODUCTION | OBJECTIVES | OVERVIEW | ARCHITECTURE | PHASES | CHALLENGES | SECURITY | RESULTS
Results Achieved
Bluetooth Device Pairing
Successful pairing between Kali Linux and Android
MAP Service Discovery
Located and identified MAP service on target
Bluetooth Communication
Established stable MAP protocol connection
SMS Event Monitoring
Real-time message interception achieved
Dashboard Integration
Flask dashboard with live event display
Firebase OTP Authentication
Complete OTP simulation system
Real-Time Visualization
Live data display and security metrics
Wireless Security Demo
Complete end-to-end attack demonstration
University Of Wah
17 / 18
Notes: This slide summarizes all the results we achieved during this project. We successfully completed all eight major milestones: Bluetooth device pairing between Kali Linux and the Android smartphone, MAP service discovery using sdptool, Bluetooth communication establishment, SMS event monitoring with real-time interception, Flask dashboard integration for visualization, Firebase OTP authentication simulation, real-time visualization of intercepted data, and a comprehensive wireless security demonstration. These results validate our research objectives and demonstrate the practical security implications of Bluetooth MAP vulnerabilities.

## Slide 18
Thank You
QUESTIONS & ANSWERS
Friendly notice:
My friend has Down syndrome and gets super excited
when people start asking him lots of questions.
If you ask him one question, be prepared for a full TED Talk! 😄
So please go easy on the questions and let him enjoy
the session comfortably. Thanks for understanding!
University Of Wah | Wireless and Mobile Security
Notes: This is our concluding slide. The project successfully demonstrated Bluetooth MAP communication and SMS event monitoring in a controlled laboratory environment. Our research highlighted critical security implications of Bluetooth permissions and SMS-based authentication systems. The key takeaway is the importance of stronger multi-factor authentication methods that do not rely on SMS, such as authenticator apps and hardware security keys. We would now like to open the floor for any questions from the audience.